## Slide 1: Finite Element Method using scikit-fem
Adam Grice

## Slide 2: Finite Element Method (FEM)
Numerical method for solving PDEs
Divides problem’s domain into smaller elements
Problem solved numerically in each element

## Slide 3: FEM--Applications
Commonplace in engineering, used for analyzing structural mechanics, fluid flow, heat transfer, mass transport, etc.
Public Domain, https://commons.wikimedia.org/w/index.php?curid=641911

## Slide 4: FEM--Terminology
Element: a single sub-domain
Mesh: collection of elements
Facet: edge of an element
Node: vertex of an element

## Slide 5: How it Works
PDE approximated algebraically in each element
  Algebraically for steady-state problems, with ODEs for transient
  Method of solution varies
Elements only affected by boundaries with their direct neighbors

## Slide 6: Implementation
Define mesh
  Size, shape, element geometry
Choose basis
  Set of functions which will approximate the PDE

## Slide 7: My Project
Take existing problem and modify it
scikit-fem has large bank of example code
Chose plate-bending problem

## Slide 8: Kirchhoff-Love Plate Bending
Equation describing deflection of isotropic, homogeneous plates
Notes: E is Young’s modulus, a measure of stiffness under tension or compression. Nu is Poisson’s ratio, a measure of deformation in directions perpendicular to load. F is load, u is deflection, and d is thickness.

## Slide 9: Original Solution
Steel plate clamped on three sides, 10cm thick
Uniform load applied at bottom edge
Notes: Force on order of 10^6 N

## Slide 10: Modified Problem
Circular-ish mesh, smaller elements
Thinner plate, 1mm thick
Clamped on border
Changed loading force to be sinusoidal

## Slide 11: Extensions and Problems
Would like to better understand how to modify mesh and B.C.s
Still in Cartesian coordinates, couldn’t figure out conversion to cylindrical

## Slide 12: My Code